## Slide 1
CCNA 5.0 Planning Guide
Chapter 2: Configuring a Network Operating System
Introduction to Networks

## Slide 2: Chapter 2: Objectives
Upon completion of this chapter you will be able to:
Explain the purpose of the Cisco IOS.
Explain how to access and navigate the Cisco IOS to configure network devices.
Describe the command structure of the Cisco IOS software.
Configure hostnames on a Cisco IOS device using the CLI.
Use Cisco IOS commands to limit access to device configurations.
Use Cisco IOS commands to save the running configuration.
Explain how devices communicate across network media.
Configure a host device with an IP address.
Verify connectivity between two end devices.
Notes: 2

## Slide 3: Chapter 2: Activities
What activities are associated with this chapter?
  2.0.1.2 Class Activity – It is Just an Operating System
  2.1.1.5 Video Demonstration – CCO Accounts and IOS Image Exploration
  2.1.2.4 Activity – Accessing Devices
  2.1.3.6 Video Demonstration – Navigating the Cisco IOS
  2.1.4.8 Packet Tracer – Navigating the Cisco IOS
  2.1.4.9 Lab – Establishing a Console Session with Tera Term
  2.2.1.4 Syntax Checker – Configuring Hostnames
  2.2.2.4 Syntax Checker – Configuring Password Encryption
  2.2.3.1 Syntax Checker – Saving Running Configuration
  2.2.3.3 Packet Tracer – Configuring Initial Switch Settings
Notes: 3

## Slide 4: Chapter 2: Activities
What activities are associated with this chapter?
  2.3.2.1 Syntax Checker – Configuring a Switch Virtual Interface
  2.3.2.3 Syntax Checker – Verifying Windows PC IP Configuration
  2.3.2.5 Packet Tracer – Implementing Basic Connectivity
  2.3.3.1 Syntax Checker – Testing the Loopback Address
  2.3.3.2 Syntax Checker – Verifying the VLAN Interface Assignment
  2.3.3.3 Syntax Checker – Testing End-to-End Connectivity
  2.3.3.4 Lab – Building a Simple Network
  2.3.3.5 Lab – Configuring a Switch Management Address
  2.4.1.1 Class Activity – Tutor Me
  2.4.1.2 Packet Tracer – Skills Integration Challenge
Notes: 4

## Slide 5: Chapter 2: Packet Tracer Activity Password
The password for all the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 2: Assessment
Students should complete the Chapter 2 Assessment after completing Chapter 2.
Worksheets, quizzes, and labs can be used to informally assess student progress.
Notes: 6

## Slide 7: Chapter 2: New Terms and Commands
What terms and commands are introduced in this chapter?
2.1.1.1 | Cisco IOS Command-line interface (CLI)
2.1.1.2 | Integrated Service Router (ISR)
2.1.1.3 | Flash memory
2.1.2.1 | Console port
2.1.2.2 | Telnet Secure Shell (SSH) Auxiliary port (AUX)
2.1.3.1 | User EXEC mode Privileged EXEC mode Global configuration mode
2.1.3.3 | Interface configuration mode Line configuration mode
2.1.3.4 | enable command disable command
2.1.3.5 | exit command end command
Notes: 7

## Slide 8: Chapter 2: New Terms and Commands (cont.)
What terms and commands are introduced in this chapter?
2.1.4.3 | Context-sensitive help
2.1.4.5 | Hot keys Shortcuts
2.1.4.6 | show commands
2.1.4.7 | show version command
2.2.1.2 | Hostnames
2.2.2.1 | enable password enable secret console password VTY password
2.2.2.2 | enable password password command enable secret password command
2.2.2.3 | line console 0 command password password command login command line vty 0 15 command
Notes: 8

## Slide 9: Chapter 2: New Terms and Commands (cont.)
What terms and commands are introduced in this chapter?
2.2.2.4 | service password-encryption command show running-config command show startup-config command
2.2.2.5 | Banners banner motd #message# command
2.2.3.1 | Running configuration Startup configuration NVRAM copy running-config startup-config command
2.3.1.1 | IPv4 IPv6 Dotted decimal notation Subnet mask
2.3.1.2 | Ethernet Local-area network (LAN) Switch virtual interface (SVI)
Notes: 9

## Slide 10: Chapter 2: New Terms and Commands (cont.)
What terms and commands are introduced in this chapter?
2.3.2.1 | IP address interface vlan 1 command ip address command no shutdown command
2.3.2.2 | Default gateway Domain name system (DNS)
2.3.3.1 | ping command Loopback
2.3.3.2 | Intermediary devices show ip interface brief command
Notes: 10

## Slide 11
Prior to teaching Chapter 2, the instructor should:
Complete the Chapter 2 Assessment.
Explain to the students that this chapter covers four basic concepts required for setting up and testing a network:
  Before configuring devices, you must know the functions of the Cisco IOS devices, learning to communicate with the IOS, and physically connecting to the devices.
  Know the basics of device configurations, including securing the device, naming devices, and enabling interfaces.
  Know the basic tools for verifying network connectivity, such as ping and traceroute.
  Know how to monitor and document a network.
Ensure that this chapter becomes as hand-on as possible.
Explain that the IOS gives networking hardware its capabilities.
Chapter 2: Best Practices
Notes: 11

## Slide 12
Demonstrate how to configure a device.
Ensure that the class knows that a router or a switch runs an IOS. Ask for volunteers to explain how access is gained to the IOS.
  Devices can be accessed via the console port (a direct physical connection), via Telnet, SSH (a virtual connection), HTTP, or via AUX (telephone modem or ISDN)).
Write and introduce the following configuration modes on the board; ask the class to explain or define these modes:
  user EXEC mode
  privilege EXEC mode
  global configuration mode
Chapter 2: Best Practices (cont.)
Notes: 12

## Slide 13
Display a router interface and demonstrate the modes and their associated prompts.
Demonstrate how to back out from privilege EXEC mode to user EXEC mode with the disable command.
Demonstrate the various forms of context-sensitive Help available.
Reinforce that show commands serve as a powerful troubleshooting tool.
Explain to the class that devices come with default names.
  Explain that names are not assigned randomly; for example, a router is named “router” by default; a switch is “switch”.
  A networking professional creates a naming convention that spans the company to maintain continuity and prepare for future growth.
Chapter 2: Best Practices (cont.)
Notes: 13

## Slide 14
Ask the class to list some naming conventions:
  Names should start with a letter names.
  Names should not contain a space.
  Names should end with a letter or digit.
  Names should have characters of only letters, digits, and hyphens.
  Names should be 63 characters or fewer.
Describe the HyperTerminal transfer options and capture text option. Also describe the implications of the speed (bps) options on HyperTerminal versus the speed options configurable either in ROMMON or on a line of a router or switch.
Chapter 2: Best Practices (cont.)
Notes: 14

## Slide 15
Explain that other than physical security of equipment, which is always necessary, there are also ways to use passwords to add additional security. On the board, write the four password types students will learn to configure in the PT Activity.
  console password – password to limit device access using the console connection.
  enable password – password to limit access to the privileged EXEC mode.
  enable secret password – encrypted password to limit access to the privileged EXEC mode.
  VTY password – password to limit device access using Telnet.
Emphasize to use the copy running-config startup-config and copy run start commands.
Chapter 2: Best Practices (cont.)
Notes: 15

## Slide 16
Encourage using different passwords for each of these access levels. From a security standpoint, requiring only one password is analogous to locking the doors to a house while leaving the windows open. Additionally, remind students to use strong passwords that are not easily guessed. The use of weak or easily guessed passwords continues to be a security issue in many facets of the business world. Ask the class how many of them have passwords that breach these best practices. There likely will be quite a few, which illustrates how common the errors are.
Describe some of the major terminal emulation programs, as Network engineers usually have a strong preference for one or the other, relating to the specific settings that can be tweaked in the terminal emulation environment (window size, fonts, colors, number of simultaneous sessions, etc.).
Chapter 2: Best Practices (cont.)
Notes: 16

## Slide 17
Explain that there are two types of configuration files:
  Startup configuration files (startup-config). These are stored in NVRAM and remain intact if the router is powered off.
  Running configuration file. Each time a router is booted up, the startup-config is loaded into RAM and becomes the second type of config file, the running configuration file (running-config). This file will change immediately if an administrator makes a change to a device. This change will cause the running-config to be different from the startup-config. Because the running-config is stored in RAM, if a power cycle takes place without saving the changes from running-config to the startup-config, any changes made will be lost.
Chapter 2: Best Practices (cont.)
Notes: 17

## Slide 18
Write the following definitions on the board and then ask the students to name the command.
  Shows the config file in RAM. This file is immediately changed if you make any changes to the router. (show running-config)
  This file is in NVRAM and will become the running-config in the event of a power cycle. (show startup-config)
  Copies the current configuration in RAM to NVRAM. (copy running-config startup-config)
  Causes the device to reload the startup-config into RAM. (reload)
  Copies the configuration in NVRAM to RAM (copy startup-config running-config)
  Causes the startup config to be erased. (erase startup-config)
Chapter 2: Best Practices (cont.)
Notes: 18

## Slide 19
Explain that when testing a network, it is best to work in a planned sequence of steps to establish valid connections, rather than to randomly jump from one place to the next.
Explain that the trace utility allows you to see the “hops” a packet takes through the network. In Windows, use the tracert command; in the CLI, use traceroute.
Pose the following questions to the class:
  What mode must you be in to make configuration changes?
  If the students erase the startup-config, what else is needed to return the device to factory default?
Emphasize to use the copy running-config startup-config and copy run start commands.
Chapter 2: Best Practices (cont.)
Notes: 19

## Slide 20
Describe the role and explain the location of the startup-config and running-config file on a switch and router.
Explain the role of IP addresses on routers in an internetwork, with emphasis on Ethernet interfaces.
Describe duplicate IP address scenarios.
Introduce a high-level description of the interfaces and ports on a switch and router.
Demonstrate with a preconfigured configuration an end-to-end connection with ping and traceroute.
Chapter 2: Best Practices (cont.)
Notes: 20

## Slide 21: Chapter 2: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at www.communities.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community to help other instructors.
Notes: 21

## Slide 22: Chapter 2: Topics Not in ICND1 100-101
This section lists topics covered by this chapter that are NOT listed in the ICND2 200-101 blueprint. Those topics are posted at http://www.cisco.com/web/learning/exams/list/icnd1b.html.
Instructors could skip these sections; however, they should provide additional information and fundamental concepts to assist the student with the topic.
Notes: 22

## Slide 23: Chapter 2: Topics Not in ICND1
What sections of this chapter are NOT in ICND1 100-101 certification blueprint?
2.0 | Section | Introduction
2.1.1 | Topic | Cisco IOS
2.2.2.5 | Page | Banner Messages
2.2.3.2 | Page | Capturing Text
2.3.1 | Topic | Ports and Addresses
2.3.2.2 | Page | Manual IP Address Configuration for End Devices
2.3.3.1 | Page | Test the Loopback Address on an End Device
2.3.3.2 | Page | Testing the Interface Assignment
2.4.1.1 | Page | Summary
Notes: 23